MANTIKSAL DEVRE TASARIMI

PROJE RAPORU

PROJE İSMİ:
VGA ÇIKIŞI İLE OYUN

Murat Kayra Meral	171101023

KOD:

vga_proje.v (ana modül)

`timescale 1ns / 1ps
module top(
    input wire CLK, // board clock: 100 MHz on Arty/Basys3/Nexys

    input wire btnL, // left button to jump
    input wire btnU, // up button to color switch
    input wire btnC, // reset the game
    output wire VGA_HS_O, // horizontal sync output 1
    output wire VGA_VS_O, // vertical sync output
    output wire [3:0] VGA_R, // 4-bit VGA red output
    output wire [3:0] VGA_G, // 4-bit VGA green output
    output wire [3:0] VGA_B // 4-bit VGA blue output
    );

    wire [9:0] x; // current pixel x position: 10-bit value: 0-1023
    wire [8:0] y; // current pixel y position: 9-bit value: 0-511
    wire _animate; // high when we're ready to animate at end of drawing

    // generate a 25 MHz pixel strobe
    reg [15:0] cnt = 0;
    reg pix_stb = 0; 2
    always @(posedge CLK) //bu kodda 25MHz lik clock olusturdu.
        {pix_stb, cnt} <= cnt + 16'h4000; // divide by 4: (2^16)/4 = 0x4000

 vga640x480 display (

        .i_clk(CLK),
        .i_pix_stb(pix_stb),
        .i_rst(rst),
        .o_hs(VGA_HS_O), 3
        .o_vs(VGA_VS_O),
        .o_x(x),
        .o_y(y),
        .o_animate(_animate)
    );

    wire player, line, jump, trig_1, trig_2a,trig_2b, trig_3, trig_4a, trig_4b, trig_5a,trig_5b, trig_6, trig_7, trig_8a, trig_8b, trig_9, trig_10a, trig_10b, trig_10c;

    wire [12:0] trig_1_upx, trig_1_upy, trig_1_leftx, trig_1_rightx, trig_1_bottomy;
    wire [12:0] trig_2a_upx, trig_2a_upy, trig_2a_leftx, trig_2a_rightx, trig_2a_bottomy;
    wire [12:0] trig_2b_upx, trig_2b_upy, trig_2b_leftx, trig_2b_rightx, trig_2b_bottomy;
    wire [12:0] trig_3_upx, trig_3_upy, trig_3_leftx, trig_3_rightx, trig_3_bottomy;
    wire [12:0] trig_4a_upx, trig_4a_upy, trig_4a_leftx, trig_4a_rightx, trig_4a_bottomy;
    wire [12:0] trig_4b_upx, trig_4b_upy, trig_4b_leftx, trig_4b_rightx, trig_4b_bottomy;
    wire [12:0] trig_5a_upx, trig_5a_upy, trig_5a_leftx, trig_5a_rightx, trig_5a_bottomy;
    wire [12:0] trig_5b_upx, trig_5b_upy, trig_5b_leftx, trig_5b_rightx, trig_5b_bottomy;
    wire [12:0] trig_6_upx, trig_6_upy, trig_6_leftx, trig_6_rightx, trig_6_bottomy; 4
    wire [12:0] trig_7_upx, trig_7_upy, trig_7_leftx, trig_7_rightx, trig_7_bottomy;
    wire [12:0] trig_8a_upx, trig_8a_upy, trig_8a_leftx, trig_8a_rightx, trig_8a_bottomy;
    wire [12:0] trig_8b_upx, trig_8b_upy, trig_8b_leftx, trig_8b_rightx, trig_8b_bottomy;
    wire [12:0] trig_9_upx, trig_9_upy, trig_9_leftx, trig_9_rightx, trig_9_bottomy;
    wire [12:0] trig_10a_upx, trig_10a_upy, trig_10a_leftx, trig_10a_rightx, trig_10a_bottomy;
    wire [12:0] trig_10b_upx, trig_10b_upy, trig_10b_leftx, trig_10b_rightx, trig_10b_bottomy;
    wire [12:0] trig_10c_upx, trig_10c_upy, trig_10c_leftx, trig_10c_rightx, trig_10c_bottomy;
    wire [12:0] trig_11_upx, trig_11_upy, trig_11_leftx, trig_11_rightx, trig_11_bottomy;

    wire [11:0] pl_x1, pl_x2, pl_y1, pl_y2;
    wire rst;

    assign rst=btnC; 5
    assign jump=btnU;
    assign animate=_animate & !coldetect;
    triangle #(.H_SIZE(23), .IX(2200), .IY(217)) trig1 (
        .i_clk(CLK),

        .i_ani_stb(pix_stb),
        .i_rst(rst),
        .i_animate(animate),
        .o_top_x(trig_1_upx), 6
        .o_top_y(trig_1_upy),
        .o_left_x(trig_1_leftx),
        .o_bottom_y(trig_1_bottomy),
        .o_right_x(trig_1_rightx)
    );
    triangle #(.IX(2750), .IY(217), .H_SIZE(23)) trig2a (
        .i_clk(CLK),
        .i_ani_stb(pix_stb),
        .i_rst(rst),
        .i_animate(animate),
        .o_top_x(trig_2a_upx),
        .o_top_y(trig_2a_upy),
        .o_left_x(trig_2a_leftx),
        .o_bottom_y(trig_2a_bottomy),
        .o_right_x(trig_2a_rightx)
    );
    triangle #(.IX(2750), .IY(171), .H_SIZE(23)) trig2b (
        .i_clk(CLK),
        .i_ani_stb(pix_stb),
        .i_rst(rst),
        .i_animate(animate),
        .o_top_x(trig_2b_upx),
        .o_top_y(trig_2b_upy),
        .o_left_x(trig_2b_leftx),
        .o_bottom_y(trig_2b_bottomy),
        .o_right_x(trig_2b_rightx)
    );
    triangle #(.IX(3300), .IY(217), .H_SIZE(23), .SPEED(10)) trig3 ( //size ucgenin yarı ebatı
        .i_clk(CLK),
        .i_ani_stb(pix_stb),
        .i_rst(rst),
        .i_animate(animate),
        .o_top_x(trig_3_upx),
        .o_top_y(trig_3_upy),
        .o_left_x(trig_3_leftx),
        .o_bottom_y(trig_3_bottomy),
        .o_right_x(trig_3_rightx)
    );
    triangle #(.IX(3700), .IY(217), .H_SIZE(23)) trig4a (
        .i_clk(CLK),
        .i_ani_stb(pix_stb),
        .i_rst(rst),
        .i_animate(animate),
        .o_top_x(trig_4a_upx),
        .o_top_y(trig_4a_upy),
        .o_left_x(trig_4a_leftx),
        .o_bottom_y(trig_4a_bottomy),
        .o_right_x(trig_4a_rightx)
    );
    triangle #(.IX(3700), .IY(171), .H_SIZE(23)) trig4b (
        .i_clk(CLK),
        .i_ani_stb(pix_stb),
        .i_rst(rst),
        .i_animate(animate),
        .o_top_x(trig_4b_upx),
        .o_top_y(trig_4b_upy),
        .o_left_x(trig_4b_leftx),
        .o_bottom_y(trig_4b_bottomy),
        .o_right_x(trig_4b_rightx)
    );
    triangle #(.IX(4500), .IY(217), .H_SIZE(23)) trig5a (
        .i_clk(CLK),
        .i_ani_stb(pix_stb),
        .i_rst(rst),
        .i_animate(animate),
        .o_top_x(trig_5a_upx),
        .o_top_y(trig_5a_upy),
        .o_left_x(trig_5a_leftx),
        .o_bottom_y(trig_5a_bottomy),
        .o_right_x(trig_5a_rightx)
    );
    triangle #(.IX(4500), .IY(171), .H_SIZE(23)) trig5b (
        .i_clk(CLK),
        .i_ani_stb(pix_stb),
        .i_rst(rst),
        .i_animate(animate),
        .o_top_x(trig_5b_upx),
        .o_top_y(trig_5b_upy),
        .o_left_x(trig_5b_leftx),
        .o_bottom_y(trig_5b_bottomy),
        .o_right_x(trig_5b_rightx)
    );
    triangle #(.IX(5050), .IY(217), .H_SIZE(23), .SPEED(10)) trig6 (
        .i_clk(CLK),
        .i_ani_stb(pix_stb),
        .i_rst(rst),
        .i_animate(animate),
        .o_top_x(trig_6_upx),
        .o_top_y(trig_6_upy),
        .o_left_x(trig_6_leftx),
        .o_bottom_y(trig_6_bottomy),
        .o_right_x(trig_6_rightx)
    );
    triangle #(.IX(5450), .IY(217), .H_SIZE(23)) trig7 (
        .i_clk(CLK),
        .i_ani_stb(pix_stb),
        .i_rst(rst),
        .i_animate(animate),
        .o_top_x(trig_7_upx),
        .o_top_y(trig_7_upy),
        .o_left_x(trig_7_leftx),
        .o_bottom_y(trig_7_bottomy),
        .o_right_x(trig_7_rightx)
    );
    triangle #(.IX(5850), .IY(217), .H_SIZE(23)) trig8a (
        .i_clk(CLK),
        .i_ani_stb(pix_stb),
        .i_rst(rst),
        .i_animate(animate),
        .o_top_x(trig_8a_upx),
        .o_top_y(trig_8a_upy),
        .o_left_x(trig_8a_leftx),
        .o_bottom_y(trig_8a_bottomy),
        .o_right_x(trig_8a_rightx)
    );
    triangle #(.IX(5850), .IY(171), .H_SIZE(23)) trig8b (
        .i_clk(CLK),
        .i_ani_stb(pix_stb),
        .i_rst(rst),
        .i_animate(animate),
        .o_top_x(trig_8b_upx),
        .o_top_y(trig_8b_upy),
        .o_left_x(trig_8b_leftx),
        .o_bottom_y(trig_8b_bottomy),
        .o_right_x(trig_8b_rightx)
    );

    triangle #(.IX(6550), .IY(148), .H_SIZE(23),.SPEED(15)) trig9 (
        .i_clk(CLK),
        .i_ani_stb(pix_stb),
        .i_rst(rst),
        .i_animate(animate),
        .o_top_x(trig_9_upx),
        .o_top_y(trig_9_upy),
        .o_left_x(trig_9_leftx),
        .o_bottom_y(trig_9_bottomy),
        .o_right_x(trig_9_rightx)
    );

    triangle #(.IX(7850), .IY(217), .H_SIZE(23), .SPEED(15)) trig10a (
        .i_clk(CLK),
        .i_ani_stb(pix_stb),
        .i_rst(rst),
        .i_animate(animate),
        .o_top_x(trig_10a_upx),
        .o_top_y(trig_10a_upy),
        .o_left_x(trig_10a_leftx),
        .o_bottom_y(trig_10a_bottomy),
        .o_right_x(trig_10a_rightx)
    );
    triangle #(.IX(7850), .IY(171), .H_SIZE(23), .SPEED(4) ) trig10b (
        .i_clk(CLK),
        .i_ani_stb(pix_stb),
        .i_rst(rst),
        .i_animate(animate),
        .o_top_x(trig_10b_upx),
        .o_top_y(trig_10b_upy),
        .o_left_x(trig_10b_leftx),
        .o_bottom_y(trig_10b_bottomy),
        .o_right_x(trig_10b_rightx)
    );
    triangle #(.IX(7850), .IY(125), .H_SIZE(23), .SPEED(11)) trig10c (
        .i_clk(CLK),
        .i_ani_stb(pix_stb),
        .i_rst(rst),
        .i_animate(animate),
        .o_top_x(trig_10c_upx),
        .o_top_y(trig_10c_upy),
        .o_left_x(trig_10c_leftx),
        .o_bottom_y(trig_10c_bottomy),
        .o_right_x(trig_10c_rightx)
    );
     triangle #(.IX(7850), .IY(169), .H_SIZE(22), .SPEED(14) ) trig11 (
        .i_clk(CLK),
        .i_ani_stb(pix_stb),
        .i_rst(rst),
        .i_animate(animate),
        .o_top_x(trig_11_upx),
        .o_top_y(trig_11_upy),
        .o_left_x(trig_11_leftx),
        .o_bottom_y(trig_11_bottomy),
        .o_right_x(trig_11_rightx)
       );
    square #(.IX(34), .IY(216), .H_SIZE(24)) _player (

        .i_clk(CLK),
        .i_ani_stb(pix_stb),
        .i_rst(rst),
        .i_animate(animate),
        7
        .o_x1(pl_x1),
        .o_x2(pl_x2),
        .o_y1(pl_y1),
        .o_y2(pl_y2)
    );
    //sekillerin cıkmasını sağladık
    assign trig_1 = ( (y<trig_1_bottomy) & (y>2*x-2*trig_1_rightx+trig_1_bottomy) & (y>-2*x+2*trig_1_leftx+trig_1_bottomy)) ? 1 : 0;

    assign trig_2a = ( (y<trig_2a_bottomy) & (y>2*x-2*trig_2a_rightx+trig_2a_bottomy) & (y>-2*x+2*trig_2a_leftx+trig_2a_bottomy)) ? 1 : 0;
    assign trig_2b = ( (y<trig_2b_bottomy) & (y>2*x-2*trig_2b_rightx+trig_2b_bottomy) & (y>-2*x+2*trig_2b_leftx+trig_2b_bottomy)) ? 1 : 0; 8
    assign trig_3 = ( (y<trig_3_bottomy) & (y>2*x-2*trig_3_rightx+trig_3_bottomy) & (y>-2*x+2*trig_3_leftx+trig_3_bottomy)) ? 1 : 0;
    assign trig_4a = ( (y<trig_4a_bottomy) & (y>2*x-2*trig_4a_rightx+trig_4a_bottomy) & (y>-2*x+2*trig_4a_leftx+trig_4a_bottomy)) ? 1 : 0;
    assign trig_4b = ( (y<trig_4b_bottomy) & (y>2*x-2*trig_4b_rightx+trig_4b_bottomy) & (y>-2*x+2*trig_4b_leftx+trig_4b_bottomy)) ? 1 : 0;
    assign trig_5a = ( (y<trig_5a_bottomy) & (y>2*x-2*trig_5a_rightx+trig_5a_bottomy) & (y>-2*x+2*trig_5a_leftx+trig_5a_bottomy)) ? 1 : 0;
    assign trig_5b = ( (y<trig_5b_bottomy) & (y>2*x-2*trig_5b_rightx+trig_5b_bottomy) & (y>-2*x+2*trig_5b_leftx+trig_5b_bottomy)) ? 1 : 0;
    assign trig_6 = ( (y<trig_6_bottomy) & (y>2*x-2*trig_6_rightx+trig_6_bottomy) & (y>-2*x+2*trig_6_leftx+trig_6_bottomy)) ? 1 : 0;
    assign trig_7 = ( (y<trig_7_bottomy) & (y>2*x-2*trig_7_rightx+trig_7_bottomy) & (y>-2*x+2*trig_7_leftx+trig_7_bottomy)) ? 1 : 0;
    assign trig_8a = ( (y<trig_8a_bottomy) & (y>2*x-2*trig_8a_rightx+trig_8a_bottomy) & (y>-2*x+2*trig_8a_leftx+trig_8a_bottomy)) ? 1 : 0;
    assign trig_8b = ( (y<trig_8b_bottomy) & (y>2*x-2*trig_8b_rightx+trig_8b_bottomy) & (y>-2*x+2*trig_8b_leftx+trig_8b_bottomy)) ? 1 : 0;
    assign trig_9 = ( (y<trig_9_bottomy) & (y>2*x-2*trig_9_rightx+trig_9_bottomy) & (y>-2*x+2*trig_9_leftx+trig_9_bottomy)) ? 1 : 0;
    assign trig_10a = ( (y<trig_10a_bottomy) & (y>2*x-2*trig_10a_rightx+trig_10a_bottomy) & (y>-2*x+2*trig_10a_leftx+trig_10a_bottomy)) ? 1 : 0;
    assign trig_10b = ( (y<trig_10b_bottomy) & (y>2*x-2*trig_10b_rightx+trig_10b_bottomy) & (y>-2*x+2*trig_10b_leftx+trig_10b_bottomy)) ? 1 : 0;
    assign trig_10c = ( (y<trig_10c_bottomy) & (y>2*x-2*trig_10c_rightx+trig_10c_bottomy) & (y>-2*x+2*trig_10c_leftx+trig_10c_bottomy)) ? 1 : 0;
    assign trig_11 = ( (y<trig_11_bottomy) & (y>2*x-2*trig_11_rightx+trig_11_bottomy) & (y>-2*x+2*trig_11_leftx+trig_11_bottomy)) ? 1 : 0;
    assign player = ( (x>pl_x1) & (x<pl_x2) & (y>pl_y1) & (y<pl_y2) ) ? 1 : 0;

    assign line = ( (y>=240) & (y<250) ) ? 1:0; 9
    reg [1:0] playercolor=1;
    reg idealbtnL=0, bayrak=1;

    reg player_white,player_orange,player_blue;
    always@(posedge CLK) begin //bayrak tus basılı değil demek.
        idealbtnL=0;
        if(btnL && bayrak) begin
        bayrak=0; 10

        idealbtnL=1;
        end
        else if(!btnL) begin
        bayrak=1;
        end

        if(idealbtnL==1 && !coldetect) begin
        playercolor=playercolor+1;
        if(playercolor==0) playercolor=1;
        end
        if(playercolor==1) begin //1=orange 2=blue 3=white
        player_orange=1;
        player_blue=0;
        player_white=0;
        end
        else if(playercolor==2) begin 11
        player_orange=0;
        player_blue=1;
        player_white=0;
        end
        else if(playercolor==3) begin
        player_orange=0;
        player_blue=0;
        player_white=1;
        end
    end
    wire coldetect;
    assign coldetect=

    (((pl_x2>trig_1_leftx & pl_x1<trig_1_rightx) & (pl_y2>trig_1_upy) & (playercolor!=3))
    | ((pl_x2>trig_2a_leftx & pl_x1<trig_2a_rightx) & (pl_y2>trig_2a_upy) & (playercolor!=1))
    | ((pl_x2>trig_2b_leftx & pl_x1<trig_2b_rightx) & (pl_y2>trig_2b_upy) & (playercolor!=1))
    | ((pl_x2>trig_3_leftx & pl_x1<trig_3_rightx) & (pl_y2>trig_3_upy) & (playercolor!=3))
    | ((pl_x2>trig_4a_leftx & pl_x1<trig_4a_rightx) & (pl_y2>trig_4a_upy) & (playercolor!=3)) 12
    | ((pl_x2>trig_4b_leftx & pl_x1<trig_4b_rightx) & (pl_y2>trig_4b_upy) & (playercolor!=2))
    | ((pl_x2>trig_5a_leftx & pl_x1<trig_5a_rightx) & (pl_y2>trig_5a_upy) & (playercolor!=2))
    | ((pl_x2>trig_5b_leftx & pl_x1<trig_5b_rightx) & (pl_y2>trig_5b_upy) & (playercolor!=1))
    | ((pl_x2>trig_6_leftx & pl_x1<trig_6_rightx) & (pl_y2>trig_6_upy) & (playercolor!=3))
    | ((pl_x2>trig_7_leftx & pl_x1<trig_7_rightx) & (pl_y2>trig_7_upy) & (playercolor!=2))
    | ((pl_x2>trig_8a_leftx & pl_x1<trig_8a_rightx) & (pl_y2>trig_8a_upy) & (playercolor!=2))
    | ((pl_x2>trig_8b_leftx & pl_x1<trig_8b_rightx) & (pl_y2>trig_8b_upy) & (playercolor!=3))
    | ((pl_x2>trig_9_leftx & pl_x1<trig_9_rightx) & (pl_y2>trig_9_upy) & (pl_y1<trig_9_bottomy) & (playercolor!=2))
    | ((pl_x2>trig_10a_leftx & pl_x1<trig_10a_rightx) & (pl_y2>trig_10a_upy) &(pl_y1<trig_10a_bottomy)& (playercolor!=1))
    | ((pl_x2>trig_10b_leftx & pl_x1<trig_10b_rightx) & (pl_y2>trig_10b_upy)&(pl_y1<trig_10b_bottomy) & (playercolor!=2))
    | ((pl_x2>trig_10c_leftx & pl_x1<trig_10c_rightx) & (pl_y2>trig_10c_upy)&(pl_y1<trig_10c_bottomy) & (playercolor!=1)))
    | ((pl_x2>trig_11_leftx & pl_x1<trig_11_rightx) & (pl_y2>trig_11_upy)&(pl_y1<trig_11_bottomy) & (playercolor!=3))
    ? 1 : 0;
    wire white,orange,blue;

    assign white=trig_1|trig_3|trig_4a|trig_6|trig_8b| trig_11| (player_white & player);
    assign orange=trig_2a|trig_2b|trig_5b|trig_10a|trig_10c|(player_orange & player);
    assign blue=trig_4b|trig_5a|trig_7|trig_8a|trig_9|trig_10b|(player_blue & player);
    assign VGA_R = 15*(line|orange|white);
    assign VGA_G[3]=(line|white); 13
    assign VGA_G[2]=(line|white);
    assign VGA_G[1]=(line|orange|white|blue);
    assign VGA_G[0]=(line|orange|white|blue);
    assign VGA_B = 15*(line|white|blue);
endmodule

triangle.v modülü
`timescale 1ns / 1ps
module triangle #(
    H_SIZE=10, // triangle half side and half height
    IX=320, // initial horizontal position of triangle centre
    IY=230, // initial vertical position of triangle centre
    IX_DIR=1, // initial horizontal direction: 1 is right, 0 is left
    IY_DIR=1, // initial vertical direction: 1 is down, 0 is up
    D_WIDTH=640, // width of display
    D_HEIGHT=480, // height of display
    SPEED=6
    )
    (
    input wire i_clk, // base clock
    input wire i_ani_stb, // animation clock: pixel clock is 1 pix/frame
    input wire i_rst, // reset: returns animation to starting position
    input wire i_animate, // animate when input is high
    output wire [12:0] o_top_x, // triangle top corner x
    output wire [12:0] o_top_y, // triangle top corner y
    output wire [12:0] o_left_x, // triangle left (bottom) corner x
    output wire [12:0] o_bottom_y, // triangle bottom y
    output wire [12:0] o_right_x // triangle right (bottom) corner x
    );

    reg [12:0] x = IX; // horizontal position of triangle centre
    reg [12:0] y = IY; // vertical position of trtiangle centre
    reg x_dir = IX_DIR; // horizontal animation direction
    reg y_dir = IY_DIR; // vertical animation direction

    assign o_top_x=x;
    assign o_top_y=y-H_SIZE;
    assign o_left_x=x-H_SIZE;
    assign o_bottom_y=y+H_SIZE;
    assign o_right_x=x+H_SIZE;

    always @ (posedge i_clk)
    begin
        if (i_rst) // on reset return to starting position
        begin
        x <= IX;
        y <= IY;
        x_dir <= IX_DIR;
        y_dir <= IY_DIR;
        end
        if (i_animate && i_ani_stb)
        begin
        x <= x-SPEED;
        end
    end
endmodule

player_square.v modülü

`timescale 1ns / 1ps
module square #(
    H_SIZE=80, // half square width (for ease of co-ordinate calculations)
    IX=320, // initial horizontal position of square centre
    IY=240, // initial vertical position of square centre
    IX_DIR=1, // initial horizontal direction: 1 is right, 0 is left
    IY_DIR=0, // initial vertical direction: 1 is down, 0 is up
    D_WIDTH=640, // width of display
    D_HEIGHT=480 // height of display
    )
    (
    input wire i_clk, // base clock
    input wire i_ani_stb, // animation clock: pixel clock is 1 pix/frame
    input wire i_rst, // reset: returns animation to starting position
    input wire i_animate, // animate when input is high
    input wire i_jump, // initiate movement when high
    output wire [11:0] o_x1, // square left edge: 12-bit value: 0-4095
    output wire [11:0] o_x2, // square right edge
    output wire [11:0] o_y1, // square top edge
    output wire [11:0] o_y2 // square bottom edge
    );

    reg [11:0] x = IX; // horizontal position of square centre
    reg [11:0] y = IY; // vertical position of square centre
    reg x_dir = IX_DIR; // horizontal animation direction
    reg y_dir = IY_DIR; // vertical animation direction
    assign o_x1 = x - H_SIZE; // left: centre minus half horizontal size
    assign o_x2 = x + H_SIZE; // right
    assign o_y1 = y - H_SIZE; // top
    assign o_y2 = y + H_SIZE; // bottom
    always @ (posedge i_clk)
    begin
        if (i_rst) // on reset return to starting position
        begin
        x <= IX;
        y <= IY;
        x_dir <= IX_DIR;
        y_dir <= IY_DIR;
        end
        if (i_animate && i_ani_stb)
        begin //kare yere temas ettiğinde aşağı düşmesini engellemek
        y <= (y_dir) ? y + 8*(y_dir) : y - 8*(i_jump); // move down if positive y_dir
        if (y <= H_SIZE + 1 || i_jump==0) // edge of square at top of screen
        y_dir <= 1; // change direction to down
        if (y >= (D_HEIGHT/2 - H_SIZE - 13)) // edge of square at bottom
        begin
        y_dir <= 0; // change direction to up
        end
        end
    end
endmodule

vga1.v modülü

`timescale 1ns / 1ps
module vga640x480(
    input wire i_clk, // base clock
    input wire i_pix_stb, // pixel clock strobe
    input wire i_rst, // reset: restarts frame
    output wire o_hs, // horizontal sync
    output wire o_vs, // vertical sync
    output wire o_blanking, // high during blanking interval
    output wire o_active, // high during active pixel drawing
    output wire o_screenend, // high for one tick at the end of screen
    output wire o_animate, // high for one tick at end of active drawing
    output wire [9:0] o_x, // current pixel x position
    output wire [8:0] o_y // current pixel y position
    );

    // VGA timings https://timetoexplore.net/blog/video-timings-vga-720p-1080p
    localparam HS_STA = 16; // horizontal sync start
    localparam HS_END = 16 + 96; // horizontal sync end
    localparam HA_STA = 16 + 96 + 48; // horizontal active pixel start
    localparam VS_STA = 480 + 10; // vertical sync start
    localparam VS_END = 480 + 10 + 2; // vertical sync end
    localparam VA_END = 480; // vertical active pixel end
    localparam LINE = 800; // complete line (pixels)
    localparam SCREEN = 525; // complete screen (lines)

    reg [9:0] h_count; // line position
    reg [9:0] v_count; // screen position

    // generate sync signals (active low for 640x480)
    assign o_hs = ~((h_count >= HS_STA) & (h_count < HS_END));
    assign o_vs = ~((v_count >= VS_STA) & (v_count < VS_END));

    // keep x and y bound within the active pixels
    assign o_x = (h_count < HA_STA) ? 0 : (h_count - HA_STA);
    assign o_y = (v_count >= VA_END) ? (VA_END - 1) : (v_count);

    // blanking: high within the blanking period
    assign o_blanking = ((h_count < HA_STA) | (v_count > VA_END - 1));

    // active: high during active pixel drawing
    assign o_active = ~((h_count < HA_STA) | (v_count > VA_END - 1));

    // screenend: high for one tick at the end of the screen
    assign o_screenend = ((v_count == SCREEN - 1) & (h_count == LINE));

    // animate: high for one tick at the end of the final active pixel line
    assign o_animate = ((v_count == VA_END - 1) & (h_count == LINE));

    always @ (posedge i_clk)
    begin
        if (i_rst) // reset to start of frame
        begin
        h_count <= 0;
        v_count <= 0;
        end
        if (i_pix_stb) // once per pixel
        begin
        if (h_count == LINE) // end of line
        begin
        h_count <= 0;
        v_count <= v_count + 1;
        end
        else
        h_count <= h_count + 1;

        if (v_count == SCREEN) // end of screen
        v_count <= 0;
        end
    end
endmodule

consvga.xdc modülü

## Clock signal

set_property PACKAGE_PIN W5 [get_ports CLK]
set_property IOSTANDARD LVCMOS33 [get_ports CLK]
create_clock -add -name sys_clk_pin -period 10.00 -waveform {0 5} [get_ports CLK]

##Buttons

set_property PACKAGE_PIN W19 [get_ports btnL]
    set_property IOSTANDARD LVCMOS33 [get_ports btnL]
set_property PACKAGE_PIN T18 [get_ports btnU]
    set_property IOSTANDARD LVCMOS33 [get_ports btnU]
set_property PACKAGE_PIN U18 [get_ports btnC]
    set_property IOSTANDARD LVCMOS33 [get_ports btnC]

#VGA Connector
set_property PACKAGE_PIN G19 [get_ports {VGA_R[0]}]
set_property IOSTANDARD LVCMOS33 [get_ports {VGA_R[0]}]
set_property PACKAGE_PIN H19 [get_ports {VGA_R[1]}]
set_property IOSTANDARD LVCMOS33 [get_ports {VGA_R[1]}]
set_property PACKAGE_PIN J19 [get_ports {VGA_R[2]}]
set_property IOSTANDARD LVCMOS33 [get_ports {VGA_R[2]}]
set_property PACKAGE_PIN N19 [get_ports {VGA_R[3]}]
set_property IOSTANDARD LVCMOS33 [get_ports {VGA_R[3]}]
set_property PACKAGE_PIN N18 [get_ports {VGA_B[0]}]
set_property IOSTANDARD LVCMOS33 [get_ports {VGA_B[0]}]
set_property PACKAGE_PIN L18 [get_ports {VGA_B[1]}]
set_property IOSTANDARD LVCMOS33 [get_ports {VGA_B[1]}]
set_property PACKAGE_PIN K18 [get_ports {VGA_B[2]}]
set_property IOSTANDARD LVCMOS33 [get_ports {VGA_B[2]}]
set_property PACKAGE_PIN J18 [get_ports {VGA_B[3]}]
set_property IOSTANDARD LVCMOS33 [get_ports {VGA_B[3]}]
set_property PACKAGE_PIN J17 [get_ports {VGA_G[0]}]
set_property IOSTANDARD LVCMOS33 [get_ports {VGA_G[0]}]
set_property PACKAGE_PIN H17 [get_ports {VGA_G[1]}]
set_property IOSTANDARD LVCMOS33 [get_ports {VGA_G[1]}]
set_property PACKAGE_PIN G17 [get_ports {VGA_G[2]}]
set_property IOSTANDARD LVCMOS33 [get_ports {VGA_G[2]}]
set_property PACKAGE_PIN D17 [get_ports {VGA_G[3]}]
set_property IOSTANDARD LVCMOS33 [get_ports {VGA_G[3]}]
set_property PACKAGE_PIN P19 [get_ports VGA_HS_O]
set_property IOSTANDARD LVCMOS33 [get_ports VGA_HS_O]
set_property PACKAGE_PIN R19 [get_ports VGA_VS_O]
set_property IOSTANDARD LVCMOS33 [get_ports VGA_VS_O]

PROJE TASARIMI

Projemiz vga_proje isimli ana modülün yanında triangle.v, player_square.v ve vga1.v isimli üç adet yan modülden oluşmaktadır.
Ana modülün içerisinde sırasıyla yapılanlar:

1. Koddaki dışarıdan bakıldığındaki giriş ve çıkışların tanımını yaptım.
2. 25MHz lik clock oluşturmayı sağladım.
3. vga1.v modülünü kullanarak görüntü almayı sağladım.
4. Üçgenlerin kenarlarını ve köşelerini tanımladım.
5. Butonlara atamalar yaptım.( Reset tuşunu centre, zıplatmayı up tuşuna atadım.) Eğer çarpma yoksa oyuna devam etmesi komutunu verdirdim.
6. Üçgenlerin ebatlarını ve konumlarını belirledim. (Özel olarak ayarladım, hızının farklı olmasını istediğimiz üçgene özel hız ataması yaptım.)(Toplamda 17 tane üçgen için aynı işlem yapıldı.)
7. Karenin (oyuncunun) ebatını ve konumunu belirttim.
8. Doğru denklemleri kullanarak eşitsizlikler sonucu üçgen ve kare şekillerini çıkarmayı başardım.
9. Yine eşitsizlik kullanarak line çıkarttırdım.
10. BtnL’ ye basıldığında çarpma da olmamışsa renk değişimi olsun kriterini sağladım.
11. Burada beyaz, turuncu ve maviyi yani bu üç renki tusa basıldıkça art arda renk değşimini sağlattım.
12. Bu kısımda yine eşitsizlik kullanarak şekillerin temas etmesi halinde çarptığını ve aynı zamanda renkler aynı olmadığında çarpma yaşandığı komutunu aldırdım.
13. Bu kısımda üç rengi elde ederek üçgenlerin herbirine, line’a, ve kareye(oyuncuya) renk sağladım. Burada renkleri şu şekilde sağladım:
1. Beyazı elde edebilmek için üç rengide kattım,
2. Turuncuyu elde edebilmek için zayıf yeşil ve parlak kırmızıyı birleştirdim,
3. Maviyi yaparken de zayıf yeşil ve parlak maviyi birleştirdim.
(Burada 15 ile çarpmamızın sebebi renklerin daha parlak olabilmesini sağlamak.)

Triangle.v isimli modülde üçgenlerin kenarlarını tanımladım, x ve y eksenindeki konum aralıklarını belirledim, üçgenlere ortak boyut ve ortak hız beliredim.

`timescale 1ns / 1ps
module triangle #(
    H_SIZE=10, // triangle half side and half height
    IX=320, // initial horizontal position of square centre
    IY=230, // initial vertical position of square centre
    IX_DIR=1, // initial horizontal direction: 1 is right, 0 is left
    IY_DIR=1, // initial vertical direction: 1 is down, 0 is up
    D_WIDTH=640, // width of display
    D_HEIGHT=480, // height of display
    SPEED=6
    )
    (
    input wire i_clk, // base clock
    input wire i_ani_stb, // animation clock: pixel clock is 1 pix/frame
    input wire i_rst, // reset: returns animation to starting position
    input wire i_animate, // animate when input is high
    output wire [12:0] o_top_x, // triangle top corner x
    output wire [12:0] o_top_y, // triangle top corner y
    output wire [12:0] o_left_x, // triangle left (bottom) corner x
    output wire [12:0] o_bottom_y, // triangle bottom y
    output wire [12:0] o_right_x // triangle right (bottom) corner x
    );

    reg [12:0] x = IX; // horizontal position of square centre
    reg [12:0] y = IY; // vertical position of square centre
    reg x_dir = IX_DIR; // horizontal animation direction
    reg y_dir = IY_DIR; // vertical animation direction

    assign o_top_x=x;
    assign o_top_y=y-H_SIZE;
    assign o_left_x=x-H_SIZE;
    assign o_bottom_y=y+H_SIZE;
    assign o_right_x=x+H_SIZE;

    always @ (posedge i_clk)
    begin
        if (i_rst) // on reset return to starting position
        begin
        x <= IX;
        y <= IY;
        x_dir <= IX_DIR;
        y_dir <= IY_DIR;
        end
        if (i_animate && i_ani_stb)
        begin
        x <= x-SPEED;
        end
    end
endmodule

player_square.v isimli modülde karemizi (yani oyuncuyu) yaptım. Bu modülde kare oluşturabilmek için x ve y ekseninde konumlar belirledim, karenin ebatını belirledik ayrıca kareye hareket sağlattım.

`timescale 1ns / 1ps
module square #(
    H_SIZE=80, // half square width (for ease of co-ordinate calculations)
    IX=320, // initial horizontal position of square centre
    IY=240, // initial vertical position of square centre
    IX_DIR=1, // initial horizontal direction: 1 is right, 0 is left
    IY_DIR=0, // initial vertical direction: 1 is down, 0 is up
    D_WIDTH=640, // width of display
    D_HEIGHT=480 // height of display
    )
    (
    input wire i_clk, // base clock
    input wire i_ani_stb, // animation clock: pixel clock is 1 pix/frame
    input wire i_rst, // reset: returns animation to starting position
    input wire i_animate, // animate when input is high
    input wire i_jump, // initiate movement when high
    output wire [11:0] o_x1, // square left edge: 12-bit value: 0-4095
    output wire [11:0] o_x2, // square right edge
    output wire [11:0] o_y1, // square top edge
    output wire [11:0] o_y2 // square bottom edge
    );

    reg [11:0] x = IX; // horizontal position of square centre
    reg [11:0] y = IY; // vertical position of square centre
    reg x_dir = IX_DIR; // horizontal animation direction
    reg y_dir = IY_DIR; // vertical animation direction
    assign o_x1 = x - H_SIZE; // left: centre minus half horizontal size
    assign o_x2 = x + H_SIZE; // right
    assign o_y1 = y - H_SIZE; // top
    assign o_y2 = y + H_SIZE; // bottom
    always @ (posedge i_clk)
    begin
        if (i_rst) // on reset return to starting position
        begin
        x <= IX;
        y <= IY;
        x_dir <= IX_DIR;
        y_dir <= IY_DIR;
        end
        if (i_animate && i_ani_stb)
        begin //kare yere temas ettiğinde aşağı düşmesini engellemek
        y <= (y_dir) ? y + 8*(y_dir) : y - 8*(i_jump); // move down if positive y_dir
        if (y <= H_SIZE + 1 || i_jump==0) // edge of square at top of screen
        y_dir <= 1; // change direction to down
        if (y >= (D_HEIGHT/2 - H_SIZE - 13)) // edge of square at bottom
        begin
        y_dir <= 0; // change direction to up
        end
        end
    end
endmodule

Vga1.v modülünde ise ekrandan görüntü alabilmek için pixel ve ekran için tanımlamalar aldım ve ekranda görüntü alabilmeyi başardım.

`timescale 1ns / 1ps
module vga640x480(
    input wire i_clk, // base clock
    input wire i_pix_stb, // pixel clock strobe
    input wire i_rst, // reset: restarts frame
    output wire o_hs, // horizontal sync
    output wire o_vs, // vertical sync
    output wire o_blanking, // high during blanking interval
    output wire o_active, // high during active pixel drawing
    output wire o_screenend, // high for one tick at the end of screen
    output wire o_animate, // high for one tick at end of active drawing
    output wire [9:0] o_x, // current pixel x position
    output wire [8:0] o_y // current pixel y position
    );

    // VGA timings https://timetoexplore.net/blog/video-timings-vga-720p-1080p
    localparam HS_STA = 16; // horizontal sync start
    localparam HS_END = 16 + 96; // horizontal sync end
    localparam HA_STA = 16 + 96 + 48; // horizontal active pixel start
    localparam VS_STA = 480 + 10; // vertical sync start
    localparam VS_END = 480 + 10 + 2; // vertical sync end
    localparam VA_END = 480; // vertical active pixel end
    localparam LINE = 800; // complete line (pixels)
    localparam SCREEN = 525; // complete screen (lines)

    reg [9:0] h_count; // line position
    reg [9:0] v_count; // screen position

    // generate sync signals (active low for 640x480)
    assign o_hs = ~((h_count >= HS_STA) & (h_count < HS_END));
    assign o_vs = ~((v_count >= VS_STA) & (v_count < VS_END));

    // keep x and y bound within the active pixels
    assign o_x = (h_count < HA_STA) ? 0 : (h_count - HA_STA);
    assign o_y = (v_count >= VA_END) ? (VA_END - 1) : (v_count);

    // blanking: high within the blanking period
    assign o_blanking = ((h_count < HA_STA) | (v_count > VA_END - 1));

    // active: high during active pixel drawing
    assign o_active = ~((h_count < HA_STA) | (v_count > VA_END - 1));

    // screenend: high for one tick at the end of the screen
    assign o_screenend = ((v_count == SCREEN - 1) & (h_count == LINE));

    // animate: high for one tick at the end of the final active pixel line
    assign o_animate = ((v_count == VA_END - 1) & (h_count == LINE));

    always @ (posedge i_clk)
    begin
        if (i_rst) // reset to start of frame
        begin
        h_count <= 0;
        v_count <= 0;
        end
        if (i_pix_stb) // once per pixel
        begin
        if (h_count == LINE) // end of line
        begin
        h_count <= 0;
        v_count <= v_count + 1;
        end
        else
        h_count <= h_count + 1;

        if (v_count == SCREEN) // end of screen
        v_count <= 0;
        end
    end
endmodule